## Slide 1: CORE-V Cores Roadmap
Davide Schiavone | davideⓐopenhwgroup.org
Jérôme Quévremont | jerome·quevremontⓐthalesgroup·com
Arjan Bink | arjan.binkⓐsilabs.com

## Slide 2: CORE-V Family History
Initial contribution of open-source RISC-V cores from ETH Zurich PULP Platform and the OpenHW Group is the official committer for these repositories
OpenHW Cores Task Group has the mandate to develop feature and functionality roadmap for the CORE-V Family of open-source RISC-V processors
  Chair: Arjan Bink, Silicon Laboratories
  Vice-Chair: Jérôme Quévremont, Thales Research & Technology
Core | Bits/Stages | Description
CV32E40P (RI5CY) | 32bit / 4-stage | A family of 4-stage cores that implement, RV32IMFCXpulp, optional 32-bit FPU, instruction set extensions for DSP operations including HW loops, SIMD extensions, bit manipulation and post-increment instructions.
CVA6 (Ariane) | 32 & 64bit / 6-stage | A family of 6-stage, single issue, in-order CPU cores implementing RV64GC extensions with three privilege levels M, S, U to fully support a Unix-like (Linux, BSD, etc.) operating system. The cores have configurable size, separate TLBs, a hardware PTW and branch-prediction (branch target buffer, branch history table and a return address stack).

## Slide 3: CORE-V P/Ns, Gates, TRLs
Reference Material

## Slide 4: CORE-V Cores P/N Syntax
CV32E40P
FAMILY
CORE-V
WL
word-length
CLASS
Embedded, Application
IDENTITY
pipe length, version
MODIFIER
special cases

## Slide 5: OpenHW Project Framework
PC
Project Concept
PL
Project Launch
PA
Plan Approved
PF
Project Freeze
Green-light of project concept by TWG
Proposed scope, initial view of the components and features, why do this project?
Purpose
Criteria
Gate
Full project launch approval by TWG
Outline of the requirements, features, components, project supporters, risks, high level schedule
Communicate project plan to TWG, (allowing member participation and review
Project plan full checklist, project methodology. initial agile backlog, requirements specification
Completion of releasable project content
RTL Freeze checklist or other final checklist has been completed
Project work

## Slide 6: TRL Scale
OpenHW Technology Outputs
OpenHW IP Adopters

## Slide 7: TRL Levels as Utilized by OpenHW
TRL | OpenHW Utilization
1- Basic Principles Observed | OpenHW research projects may target TRL-1 as project output, e.g. to develop novel approaches to core or accelerator architecture
2- Concept Formulation | Core IP or accelerator development projects to produce open source technology are typically initiated as TRL-2 concepts, identifying principles and applications of the IP The OpenHW Project Concept Gate output includes a TRL-2 description of the Core IP
3- Proof of Concept | Core IP or accelerator development projects will pass through TRL-3 as the (RTL) design completes. Poof of concept is shown by core compilation and demonstration of basic operations (e.g. Linux booted, Coremark results, hello-world)
4- Component Prototype | Core IP or accelerator projects will pass through TRL-4 as they produce preliminary PPA results (via synthesis scripts for FPGA or ASIC) and/or run preliminary application code, such as an accelerator running machine learning code.
5- Subsystem Designed and Tested | Core IP projects reach TRL-5 as they complete full verification. The OpenHW RTL Freeze checklist process verifies that the design is fully ready for industrial adoption.
6- Functional (Alpha) Prototype | OpenHW designed IP that is integrated into an MCU system or other device reaches TRL-6 as prototype Silicon is fabricated and demonstrated
7- Field Demonstration Prototype | OpenHW development boards incorporating a prototype Silicon system with OpenHW Software reach TRL-7 as they are demonstrated and deployed

## Slide 8: CORE-V RISC-V Cores Roadmap
CVA6
CVE4
CVE2
CV32E40P
RV32IM[F]CZicount_Zicsr_Zifencei [PULP_XPULP][PULP_CLUSTER][PULP_ZFINX]
4-stage, M-mode, CLINT, OBI
CV32E20
RV32[I|E][M]CZicount_Zicsr_Zifencei[_Zce]
2-stage, M-mode, [CLINT|CLIC], OBI
20Q4
21Q2
22Q2
21Q4
22Q4
CV32E40P (‘tag::v2’)
Completion of of PULP_XPULP, F
CVA6
RV{32|64}IMAC[FD]Zicsr
6-stage, M/S/U-mode, CLINT, AXI, MMU, I$, D$
FPGA-optimized flavor for CV32A6, eXtension interface considered, FENCE.T instruction considered
CV32E40S
RV32IMC[Xsecure]Zicsr_Zifencei[_Zce]
4-stage, M/U-mode, CLINT, OBI, PMP, Security
CV32E40X
RV32IM[A][F]C[B][P][X]Zicount_Zicsr_Zifencei[_Zce]
4-stage, M-mode, CLINT, OBI, eXtension interface
Project Freeze PF
Plan Approved PA
Project Concept PC
Project Launch PL
Application
Embedded

## Slide 9: CORE-V Embedded-class Cores

## Slide 10: CV32E40P – PF / TRL 5
4-stage, in-order, single-issue
RV32IM[F]CZicount_Zicsr_Zifencei [PULP_XPULP][PULP_CLUSTER][PULP_ZFINX]
M-mode, CLINT, OBI
‘RTL Freeze’ achieved
  RV32IMC extensions verified
  Step&Compare with Imperas as reference model (100% coverage)
  Interrupts and Debug
Activities on RVFI interface
  Facilitating sim-based step&compare verification FSM and formal verification

## Slide 11: CV32E40P – preliminary PPA
CV32E40P
  COREMARK/MHz: 2,91
Technology | Frequency | Area | Comments
TSMC 16nm | 909MHz | 53,4kGE | No FPU

## Slide 12: CORE-V MCU with CV32E40P
MCU that includes CV32E40P, memories, and peripherals
  based on PULPissimo from ETH
Production of the CORE-V MCU SoC in Globalfoundries GF22FDX will take CV32E40P towards TRL 6
FPGA prototype available on a Genesys 2 board

## Slide 13: CV32E40P tag::v2 – PL / TRL 3
RV32PULP_XPULP extensions
  Verification and Reference Model
  Moving the existing instructions to the RISC-V custom space
  SW support with upstream GCC and LLVM compiler
  LEC to v1 when PULP_XPULP=0
RV32F extensions
  Verification
CV-DBG
  Moving, documenting, and verifying the external RISC-V Debug module
Project goal: industrial grade (TRL 5)

## Slide 14: CV32E40P tag::v2 – preliminary PPA
CV32E40P with PULP_XPULP
  COREMARK/MHz: 3,19
Technology | Frequency | Area | Comments
UMCL 65nm | 560MHz | 40,7kGE | No FPU – based on RI5CY
Globalfoundies GF22FDX | 938MHz* | N/A | No FPU – based on RI5CY
TSMC 16nm | 769MHz | 84,5kGE | No FPU, 1 extra Perf. Counter
Xilinx Genesys 2 | 20MHz** | 7kLUTs 2,5kFFs 7 DSP | No FPU
Zynq Ultrascale+ | 140MHz | 8,4kLUTs 2,7kFFs 7 DSP | No FPU – based on RI5CY
*freq in PULPissimo on SCMs and use of Forward Body-Bias **freq with FPU in PULPissimo, not max frequency |  |  | 

## Slide 15: CV32E40S – PA / TRL 2
4-stage, in-order, single-issue
RV32IMC[Xsecure]Zicsr_Zifencei[_Zce]
M/U-mode, CLINT, OBI, ePMP, PMA, bus error
Secure core
  Reduction of side-channel attacks
  _Zce (iff ratified)
  PPA optimizations wrt CV32E40P
Verification
Project goal: industrial grade (TRL 5)

## Slide 16: CV32E40X – PA / TRL 2
4-stage, in-order, single-issue
RV32IMC[ABP]Zicount_Zicsr_Zifencei[_Zce][X]
M-mode, CLINT, OBI, PMA, bus error
Compute intensive core
  CV-X-IF interface to offload custom extensions
  _Zce, RV32B and RV32P (iff ratified)
  PPA optimizations wrt CV32E40P
Verification
Project goal: industrial grade (TRL 5)

## Slide 17: CV32E20 – PC / TRL 1
2-stage, in-order, single-issue
RV32{I,E}[M]CZicount_Zicsr_Zifencei[_Zce]
M-mode, [CLIC, CLINT], OBI
Low area core
  Optimized power and area for control-oriented applications
  Starting point lowRISC Ibex (which started from ETH zero-riscy)
    Clean-up parameters
    Aligning IP interface with CV32E40* cores
Project goal: industrial grade (TRL 5)

## Slide 18: CORE-V Application-class Cores

## Slide 19: CVA6
6-stage, in-order, single-issue
RV{32|64}IMAC[FD]Zicsr
M/S/U-mode, CLINT, AXI
Flexible application core
  Linux-compatible thanks to MMU
  32 or 64 bit (CV32A6, CV64A6) from same RTL (64b from ETH, 32b from Thales)
  L1 caches
Project goal: industrial grade (TRL 5)
  Currently drafting specifications, entry point for next stages

## Slide 20: CV64A6 – PA / TRL 4
Verification
  RV64GC (RV64IMAFDC), debug, interrupts, privileges… to verify
  sim-based Step&Compare, formal verification considered
  RVFI interface
New documentation
  reStructured text-based as for the other cores
FPGA optimizations
  Target the Xilinx Genesys2, but not a Soft-Core!

## Slide 21: CV32A6 – PA / TRL 3
32b version support for
  Pipeline
  MMU
  Floating-point
  Linux
Verification
  RV32GC (RV32IMAFDC), debug, interrupts, privileges… to verify
  sim-based Step&Compare, formal verification considered
  RVFI interface
PPA optimizations
  ASIC
  FPGA (vendor-independent soft-core)

## Slide 22: CVA6 – preliminary PPA
CV64A6
  COREMARK/MHz: 2,19
  DMIPS/MHz: 1,53
Technology | Frequency | Area | Comments
Globalfoundies GF22FDX | 1,7GHz | 210kGE | No FPU, No Caches
28nm | 740MHz | 211kGE | No FPU, No Caches
Zynq Ultrascale+ | 95MHz | 39,7kLUTs 23,2kFFs 37 DSP 37 BRAM (cache) | 

## Slide 23: CVA6 – preliminary PPA
CV32A6
  COREMARK/MHz: 2,25
  DMIPS/MHz: 1,35
Technology | Frequency | Area | Comments
28nm | 740MHz | 87kGE | No FPU, No Caches, smaller CSR config., multicycle MUL, No MMU, No branch prediction, smaller scoreboard
Zynq Ultrascale+ | 120MHz | 13,9kLUTs 9,3kFFs 4 DSP 32 BRAM (cache) | No FPU, No Caches, No MMU

## Slide 24: CORE-V Core Logic Blocks
IP surrounding the CORE-V COREs

## Slide 25: CORE-V Core Logic Blocks
Core Logic
CV-DBG
20Q4
21Q2
22Q2
21Q4
22Q4
CV-FPU
Project Freeze PF
Plan Approved PA
Project Concept PC
CV-VEC
Project Launch PL

## Slide 26: CV-FPU – PL / TRL 3
Standalone co-processor that computes floating-point RISC-V RVF and RVD extensions
  Parts of other projects as
    CV32E40Pv2, CV32A6, CV64A6
Possible starting point ETH fpnew:
  Documentation
    resTructured text documentation
  Verification stand-alone or as part of the cores
Project goal: industrial grade (TRL 5)

## Slide 27: CV-DBG – PL / TRL 3
Standalone IP that implements RISC-V Debug Module
  Debug Transport Module, and ROM for Execution based debug
  Parts of other projects as
    CV32E40Pv2, CV32A6, CV64A6
Possible starting point ETH riscv-dbg:
  Documentation
    resTructured text documentation
  Verification stand-alone or as part of the cores
Project goal: industrial grade (TRL 5)

## Slide 28: CV-VEC – PC / TRL 3
Standalone co-processor that computes vectorial instructions based on RISC-V RVV extensions
Starting point ETH ara
  RVB vector extensions and mixed-precision
  SW support for ML applications
  Implementation in Globalfoundries 22FDX
  Compatible with CV64A6
Part of OpenHW Accelerate research program with Mitacs, CMC Microsystems, Polytechnique Montréal & ETH Zurich  TRL 4

## Slide 29: CORE-V SPECs
Specifications for RISC-V COREs

## Slide 30: Open Bus Interface (OBI) Spec
Memory Bus spec for RISC-V cores
  Handshake based on ARM AMBA AXI
  Coupled Read-Write channels
  Easily translatable to ARM AMBA protocols
    AXI, AHB
  Based on: https://raw.githubusercontent.com/openhwgroup/core-v-docs/master/cores/cv32e40p/OBI-v1.0.pdf

## Slide 31: CV-X-IF Spec
Bus spec to allow RISC-V cores to offload RV extensions
  CV32E40X will leverage this interface the most
  CV32E40P and CVA6 will evaluate it
  Based on: https://github.com/pulp-platform/riscv-extension-interface
Verification
  Formal verification needed to test the spec
Allows the cores to be agnostic about the custom extension definition

## Slide 32: and
OpenHW Group is a not-for-profit, global organization driven by its members and individual contributors where HW and SW designers collaborate in the development of open-source cores, related IP, tools and SW such as the CORE-V Family of open-source RISC-V cores
OpenHW Group & CORE-V Family of open-source RISC-V cores for use in high volume production SoCs
  Visit the OpenHW CORE-V Cores GitHub repository and contribute
  Learn more at OpenHW TV
Follow us on Twitter @openhwgroup & LinkedIn OpenHW Group