## Slide 1
CSR Access Tests
Henrik Fegran henrik.fegran@silabs.com
Disclaimer: Work in progress
1
August 2022
© OpenHW Group

## Slide 2
Outline
Current State of Affairs
Proposals
Example
August 2022
© OpenHW Group
2

## Slide 3
What is the current state of affairs?
- Incomplete CSR description yaml.
- Cumbersome update process.
  Update CSR file.
  Regenerate test.
  Requires non-automated modifications.
- Registers used in test are static.
- Does not handle design parameterization well (at all).
+ Recent WARL-handling added by lowRISC to RISCV-DV.
August 2022
© OpenHW Group
3

## Slide 4
Incomplete CSR Description YAML
RO registers are omitted.
Parameter guarded CSRs.
  CLIC registers.
  Zc registers.
  PMP registers.
  Mhpmcounter registers.
  (…) Future additions.
Result: Hard to maintain Yaml, documentation lacking, need a more self-documenting flow.
August 2022
© OpenHW Group
4

## Slide 5
Cumbersome Update Process
Run gen_csr_test.py from riscv-dv directory.
  Not directly compatible with core-v-verif test env.
  Not a very user-friendly approach.
    Script not visible until riscv-dv repository has been cloned.
    Could be more intuitive…
Add license header, preamble and a few modified assembly functions to the resulting file.
Rename file, move to correct location.
Commit and create PR to git.
March 2021
© OpenHW Group
5

## Slide 6
Proposal
Introduce wrapper script (Python)
  Generate tests on the fly, no need to use checked-in test.
    Added benefit of better coverage, as random source/destination registers are used for each run.
  Automate the required manual alterations to the generated code with a template.
  Added comment-based tags for preprocessing – currently: ### COND <Feature> [<optional threshold>] (…) ### ENDCOND.
  Could also use the C preprocessor, but python-based approach might be more maintainable.
March 2021
© OpenHW Group
6

## Slide 7
Example
Enable-tag to include registers based on command line parameters:
Alternatively, threshold for N number of feature registers:
August 2022
© OpenHW Group
7