## Slide 1: Verification Task Group October 7, 2021
Steve Richmond steve.richmond@silabs.com
Robert Chu robertchu@futurewei.com
Mike Thompson mike@openhwgroup.org

## Slide 2: Outline
Administration
General news
Call for community
Infrastructure updates
  Test program builds
  PMA randomization
  Regression support for configurations
E41/E40Pv2/A6 Updates
FPU verification
Open issues

## Slide 3: Administration
Reminder that attendance will be taken at all meetings
  Attendance ensures voting eligibility per OpenHW bylaws
Active project engagement – please reach out to get involved
  CVA6 (Jerome Quevremont/Mike Thompson)
  Force ISG (Robert Chu)
  CV32E40X/CV32E40S (Steve Richmond)

## Slide 4: News
Next week: Launch of the cv32e40s/dev branch
Merge cycles: Goal to start every other Thursday
  One has started this morning
Many thanks to Henrik Fegran (@silabs-hfegran) for the PMA randomization efforts!

## Slide 5: Call for Community
We have lots of tasks that could be addressed by the OpenHW Community!
  We are here to support – contact Steve or Mike to get involved!
Add the 1.0 bitmanip to Google riscv-dv!
  https://github.com/openhwgroup/core-v-verif/issues/923
Add LLVM to our test flow!
  https://github.com/openhwgroup/core-v-verif/issues/844
Add the latest RISC-V architecture test infrastructure!
  (This is the replacement of the compliance suite)
    This needs to be scoped to determine whether to move to the latest Python test methodology
  https://github.com/openhwgroup/core-v-verif/issues/819
  https://github.com/openhwgroup/core-v-verif/issues/818

## Slide 6: Test Program Build
Goals:
  Enable crossing of core configurations with firmware test builds
  Enable parallel firmware test builds
  Allow for custom linker scripts with random corev-dv tests
  No more generated files in the source tree
  This includes the BSP
New path for firmware build output products:
  <sim>_results/<cfg>/<test>/<run_index>/test_program/…
  Examples
    cv32e40x/sim/uvmt/xrun_results/default/hello-world/0/test_program
    cv32e40x/sim/uvmt/vsim_results/pma_test_cfg_1/corev_rand_instr_test/test_program
    cv32e40x/sim/uvmt/xrun_results/default/pma

## Slide 7: Test Program Build
Individual test build outputs: (example for run_index == 1)
  corev_rand_instr_test_1.S
  corev_rand_instr_test_1.elf
  corev_rand_instr_test_1.hex
  corev_rand_instr_test_1.itb
  corev_rand_instr_test_1.objdump
  corev_rand_instr_test_1.readelf
  linkcmds.dbgsec
  linkcmds.memory
  link.ld
  linkcmds.fixadd
  linkcmds.dbgsec

## Slide 8: Test Program Build
Linker scripts are generated in corev-dv
  linkcmds.memory -> Defines the memory sections (ram or multiple regions, dbg, nmi)
  linkcmds.pmasec -> Maps regions from riscv-dv to memory sections
  linkcmds.fixadd -> Maps fixed addresses from plusargs to handlers (boot, vector, NMI)
  linkcmds.dbgsec -> Maps debug regions (code, exception, etc.)
link.ld includes the above and is hardcoded at:
  link_corev-dv.ld
  If a core does not support address randomization then symlink link_corev-dv.ld to standard link.ld

## Slide 9: Test Program Build
Configuration support for PMA
The linker script outputs are fixed for a PMA configuration
Each PMA test configuration defines compile args and run-time plusargs
corev-dv and UVMT testbench use these plusargs
Example from:
  cv32e40x/test/cfg/pma_test_cfg_4.yaml

## Slide 10: Test Program Build
corev-dv, UVMT and RTL import the parameters from the same package to set the actual PMA parameters
  uvmt_cv32e40x_constants.sv

## Slide 11: Test Program Build
TBD
  Move mtvec handler into “static” location (similar to boot, NMI)
    Solves issue of exceptions received right after boot
    riscv-dv dynamically sets mtvec a handful of instructions into the test program

## Slide 12: Regression support for configurations
More parameters will continue to be used in our cores
  (CFG=<>) in make calls
Need to add these configurations to regressions in a scalable way
New tag (builds) added to YAML that can take a list of configurations to regress against
Extended support to Metrics, shell script and vManager output templates
  Metrics and vManager will parallelize the builds

## Slide 13: Regression support for configurations

## Slide 14: Regression support for configurations

## Slide 15: Open Issues
Note: These are repeats from last month – no progress
Logging control
  RVFI/RVVI emits a lot of logs
    Example: hello-world now emits 18M of logs (cv32e40p -> 2M of logs)
  Need to create control mechanism to control logs
  Regression – no logs by default?
  Recreate logs locally or in rerun (Metrics)
Plusarg registrations
  Validate that user supplied plusargs (YAML or make command line) are supported to avoid misspellings
  Documentation for supported plusargs
  Singleton class definition to register, parse and fetch plusargs