## Slide 1: Verification TG – E* Core Status May 20, 2021
Steve Richmond steve.richmond@silabs.com

## Slide 2: Outline
Administration
ISS
RVFI/RVVI Status
CV32E40X/S Status
Completed Tasks
Active Tasks
Next Tasks
Open Issues

## Slide 3: Administration
This will be a monthly meeting on general E-core status and project coordination
  Since meetings are monthly (1st and 3rd Thursday) VTG may not meet every other Thursday – check Mattermost for announcements or openhwgroup.org Task Group calendar
Reminder that attendance will be taken at all meetings
  Attendance ensures voting eligibility per OpenHW bylaws
Active project engagement – please reach out to get involved
  CVA6 (Jerome Quevremont/Mike Thompson)
  Force ISG (Robert Chu)
  CV32E40P_v2 (John Martin/Greg Tumbush)
  CV32E40X/CV32E40S (Steve Richmond)

## Slide 4: General Updates
Currently there is an issue with Metrics and release check scripts
  mip assertion fire w/ WFI tests
  Does not appear in Questa/Xcelium
Metrics delivered new version to fix SVA issue in E40X
  Both E40P and E40X updated
Completing merge cycle today dev->master->dev
Imperas model updates will be integrated to E40X today
  Alleviates some licensing issues

## Slide 5: RVFI/RVVI Status
Goal: Migrate module-based Step-And-Compare into UVM testbench with standard RVFI RVVI interfaces to RTL and RM
Halfdan Bechmann @ SiLabs is implementing RVFI for the CV32E40X
  https://github.com/silabs-halfdan/cv32e40x/tree/rvfi_integration
Steve Richmond @ SiLabs is implementing RVFI/RVVI in the testbench
  https://github.com/openhwgroup/core-v-verif/tree/rvfi_rvvi_initial_e40x
  Common.mk in this branch points to above RTL branch/commit

## Slide 6: RVFI/RVVI Status
Branches are runnable (must set USE_RVVI=1)
Status:
  PC/GPR checks are working w/ random stalls – all random instr tests
  Some debug interactions being debugged (RVFI signaling)
TBD:
  CSR checks
  Fix “hacks” to signal interrupts/debug request
    Currently extended RVVI to use Imperas-only signals-these need to be integrated into RVVI

## Slide 7: Completed Tasks
PMA Vplan
  https://github.com/openhwgroup/core-v-verif/issues/561
Bus error Vplan
  https://github.com/openhwgroup/core-v-verif/issues/560

## Slide 8: Active Tasks
RVFI/RVVI
  UVM step-and-compare with PC/GPR checks
    https://github.com/openhwgroup/core-v-verif/issues/611
  UVM step-and-compare with interrupt/debugreq integrated into RVVI
    https://github.com/openhwgroup/core-v-verif/issues/612

## Slide 9: Next Tasks
RVFI/RVVI
  Document RVFI/RVVI and UVM-based step-and-compare
    https://github.com/openhwgroup/core-v-verif/issues/614
  UVM-based step-and-compare with CSRs
    https://github.com/openhwgroup/core-v-verif/issues/613
Integrate OBI UVM Memory model

## Slide 10: Open Issues?