## Slide 1: Verification TG – E* Core Status October 21, 2021
Steve Richmond steve.richmond@silabs.com

## Slide 2: Outline
Administration
CV32E40X
  Active Tasks
  Next Tasks
  Formal
CV32E40S
  Active Tasks
Open Issues

## Slide 3: Administration
This will be a monthly meeting on general E-core status and project coordination
Reminder that attendance will be taken at all meetings
  Attendance ensures voting eligibility per OpenHW bylaws

## Slide 4: General Updates
CV32E40X
  Used internal irq_ack and irq_id in interrupt infrastructure (705)
    Simple connection change
  PMA address randomization added to core-v-verif and configurations (873)
  Interrupt plan refreshed (678)
  LLVM/clang support added to environment and B extension directed test (844)
    Documentation in progress
    Will present more details at next VTG

## Slide 5: CV32E40X – Active Tasks
Project task board updated:
  https://github.com/openhwgroup/core-v-verif/projects/11
Implement fence.i assertions (963)
  PR review in progress
Implement fence.i directed test (964)
  PR review in progress
  Add self-modifying test and fence.i tests to exercise/turn-on the assertions

## Slide 6: CV32E40X – Active Tasks
Implement counters tests (965)
  PR review in progress
  Update the counter tests that are failing in cv32e40x
  Add tests for interrupt event counting
  Add tests to cover new events
  NOT implementing a scoreboard or full-time checker

## Slide 7: CV32E40X – Active Tasks
Implement random instruction bus errors (872)
  Injecting random OBI-I errors – done
  corev-dv update to enable exceptions at time 0 – done
    Accomplished by adding a bootstrap routine at fixed location to jump to random mtvec
  riscv-dv program structure does not allow multiple exception to be recoverable, so random tests will only issue single bus error that is unrecoverable
    Added one-shot error mode to OBI memory agent – done
  Debug random test issues – in progress

## Slide 8: CV32E40X – Next Tasks
Port compliance test to architecture test framework (530)
Create vplan for Zce (870)
Add random corev-dv data bus errors (966)
  One-shot NMI mode configuration
  Test NMI/RVFI to RVVI signaling when update released by Imperas
  Ensure that OBI data bus errors propagate to RVFI/NMI entry

## Slide 9: CV32E40X - Formal
OpenHW staff currently bringing up OneSpin RISCV formal tool on CV32E40P - done
  Runs on OpenHW cloud
CV32E40X testbench update for the new pipeline – in progress

## Slide 10: CV32E40S – In progress
Stand up cv32e40s/dev and cv32e40s/release (874)
  All cv32e40x updates ported into cv32e40s
  PR in progress to merge updates to master
  Will stand up CIs and cv32e40s/dev and cv32e40s/release branches when complete

## Slide 11: Open Issues?