## Slide 1: Verification TG – E* Core Status November 18, 2021
Steve Richmond steve.richmond@silabs.com

## Slide 2: Outline
Administration
CV32E40X
  Active Tasks
  Next Tasks
  Formal
  Coverage
CV32E40S
  Active Tasks
Imperas
Open Issues

## Slide 3: Administration
This will be a monthly meeting on general E-core status and project coordination
Reminder that attendance will be taken at all meetings
  Attendance ensures voting eligibility per OpenHW bylaws

## Slide 4: General Updates
CV32E40X
  Continued regression updates/fixes for PMA/address randomization (various PRs)
  fence.i verification infrastructure and tests implemented
  Various fixes to debug and interrupt assertions
  Instruction/data bus error random tests progressing
  PRed 1.0.0 Zb* updates to riscv-dv
  Implement counters tests (965)
    Coverage updated, new events added to directed tests

## Slide 5: CV32E40X – Active Tasks
Project task board updated:
  https://github.com/openhwgroup/core-v-verif/projects/11
Implement random instruction bus errors (872)
  RVFI update required to discern instruction bus error cause in debug mode (to enter debug exception mode)
    Previous methodology relied on mcause, but mcause is not updated architecturally in some modes
    Can hide overlapping corner cases of exceptions
    The RVFI trap signaling will be enhanced to better cover all of these corner cases

## Slide 6: CV32E40X – Active Tasks
Add random corev-dv data bus errors (966)
  RVFI was updated to fix issue with signaling NMI in dcsr
  Random data bus errors in debug mode regressing well
  Debugging some lingering corner cases
Implement privileged spec 1.12 (1027)
  Add switch to core control config to select privileged spec
  Add CSRs to riscv-dv
  Add properties for any new CSR functionality
  Ensure release check passes

## Slide 7: CV32E40X – Next Tasks
Port compliance test to architecture test framework (530)
Create vplan for Zce (870)
Update debug vplan to v1.0.0 specification for cv32e40x (679)

## Slide 8: CV32E40X - Formal
OneSpin RISCV formal verification running on the CV32E40P and CV32E40X in OpenHW cloud
Tests are passing
Next steps
  Generate report on properties being run
  Create CI process to periodically run against CV32E40X
  Run against CV32E40S
  Extend test to other extensions/configurations

## Slide 9: CV32E40X - Coverage

## Slide 10: CV32E40X - Coverage
Block
  New privileged spec CSRs
  Mhpmcounter
  Zb* instruction turnon
    sext, clmul
  Ebreak corner case
FSM
  Missing RESET->RESET arc in controller FSM and debug FSM

## Slide 11: CV32E40X - Coverage
Assertion
  OBI assertions need to be further parameterized for unsupported features
  gnt and ready signaling need to be added
  Atomics not implemented
Covergroups
  Filter PMA configurations
  Filter OBI for unsupported features
  Interrupt instruction coverage model is reporting 0 (broken)
  ISACOV – 45.74%
    Needs validation work
    Merge issue?
    Lack of random tests for Zb*

## Slide 12: CV32E40S – In progress
Cv32e40s/dev and cv32e40s/release branches are created
CIs are running
Merging CV32E40X testbench updates to cv32e40s branches on merge cycle (every other Thursday, completed last week)

## Slide 13: Open Issues?