## Slide 1: CVFPU
Pascal Gouédo
Mike Thompson

## Slide 2: Origin
FPnew developed by ETH
Donated to OpenHW group in May 2022 to become CVFPU
Support different Floating-Point precisions, formats, Packed-SIMD, pipeline stages, Implementation through parameters.

## Slide 3: Documentation & Parameters
Specification
  https://github.com/openhwgroup/cvfpu/blob/develop/docs/README.md

## Slide 4: CVFPU configurations for CV32E40Pv2 and CVA6

## Slide 5: Verification
Formal Verification
  OneSpin proposes 2 Formal Verification App
    RISC-V Processor Verification App with F extension
    Floating-Point App (all instructions but DIV/SQRT)
    As FP instructions decoding is done inside CV32E40P core and controls are propagated to CVFPU through APU interface, Processor app will be run on a CV32E40P + CVFPU wrapper.
CV32E40P core-v-verif environment
  DIV/SQRT will be verified using core-v-verif and RISC-V DV test generator.

## Slide 6: CVFPU status
DIV rounding modes and flags are not respecting IEEE 754 in some corner cases.
  ETH is currently evaluating it and testing new DIV/SQRT unit coming from the T-head open core to replace actual one.
Formal verification started in June 2022 and should last until end of August 2022.
DIV/SQRT : Sync-up with Thales (and ASTC-Design?)